STEREO/HET User’s Guide

10/22/04

Larry Ryan

This manual is written as a complement to other HET documents already in existence.

PHASIC Channels Used on HET Boards

|  | Engineering Model | Flight Model 1 | Flight Model 2 |
| --- | --- | --- | --- |
| Detector | PHASIC | Channel | PHASIC | Channel | PHASIC | Channel |
| H1i | 0 | 1 | 0 | 1 | 0 | 1 |
| H1o | 0 | 11 | 0 | 11 | 0 | 10 |
| H2 | 1 | 1 | 1 | 3 | 1 | 2 |
| H3 | 1 | 6 | 1 | 5 | 1 | 5 |
| H4 | 1 | 8 | 1 | 7 | 1 | 7 |
| H5 | 1 | 9 | 1 | 9 | 1 | 10 |
| H6 | 1 | 12 | 1 | 12 | 1 | 13 |

Commands to Run from GSE

| Command | PHA chip | PHA channel | Hex bytes | # of bits | Description | Default in HET initial command string |
| --- | --- | --- | --- | --- | --- | --- |
| phacont | 0-1 | 0-F | x | 4 | hg-adc-en, lg-adc-en, verbose, power-on | Channels in use set to d, all unused channels set to 0 |
| tpfbsel | 0-1 | 0-F | xxx | 9 | test-enable, testsel3,2,1,0, fbsel3,2,1,0 | H1i, H1o, H2, H6 set to 6; H3, H4, H5 set to C |
| inresel | 0-1 | 0-F | xxxx | 13 | fdgsel2,1,0, indac9,…,0 | H1i, Hio, H2, H6 set to 1c30; H3, H4, H5 set to 1c60 |
| hgthrsel | 0-1 | 0-F | xxx | 10 | ioff9,…,0 (for high gain channel) | All channels set to provide lowest possible threshold |
| lgthrsel | 0-1 | 0-F | xxx | 10 | ioff9,…,0 (for low gain channel) | All channels set to provide lowest possible threshold |
| scopesel | 0-1 |  | xxx | 9 | scopesel7,…,0, scope-enable | 000 |
| presel | 0-1 |  | xx | 5 | presel3,2,1,0, preout-enable | 00 |

‘phacont’ Command

The ‘phacont’ command is used like this:

phacont  x  y  z

x = PHASIC # (0 or 1)

y = channel # (0 to F)

z = see table below for most common values to use

| z | Description |
| --- | --- |
| 0 | Turn off channel completely |
| 1 | Disable HG and LG ADC’s, but leave channel turned on |
| 7 | Disable HG ADC, enable LG adc |
| b | Enable HG ADC, disable LG adc |
| d | Enable HG and LG ADCs, verbose mode off (default at boot-up) |
| f | Enable HG and LG ADCs, verbose mode on |

‘tpfbsel’ Command

The ‘tpfbsel’ command is used like this:

tpfbsel  x  y  z

x = PHASIC # (0 or 1)

y = channel # (0 to F)

z = see table below for most common values to use

| z | Description |
| --- | --- |
| 6 | Disable test pulser, set feedback capacitor to 30pF, and set test input capacitor to 0pF (default at boot-up for H1i, H1o, H2, H6) |
| c | Disable test pulser, set feedback capacitor to 60pF, and set test input capacitor to 0pF (default at boot-up for H3, H4, H5) |
| 166 | Enable test pulser, set feedback capacitor to 30pF, and set test input capacitor to 18pF |
| 1cc | Enable test pulser, set feedback capacitor to 60pF, and set test input capacitor to 36pF |

Note that currently the software boots up with the test pulsers disabled and the test input capacitors set to 0.  For flight, you will want the test pulsers enabled and the test input capacitors set to the same hex setting as the feedback capacitors (6 for H1i, H1o, H2, H6; c for H3, H4, H5).  Using the same hex setting for feedback and test input capacitors allows the test pulser DAC to probe the full dynamic range of the HG and LG channels.  More on that below in the description of the ‘testp’ command.

‘inresel’ Command

The ‘inresel’ command should generally not be used, since the software automatically sets the indac values (input current DAC to balance detector leakage current).

‘hgthrsel’ and ‘lgthrsel’ Commands

These commands will generally not be used, since the thresholds have been set.  The current threshold values are programmed into the software and will display on the housekeeping page.  They should only be changed (increased) if the noise goes up.

‘scopesel’ and ‘presel’ Commands

These commands are only useful on the Engineering Model now, and they are described in Rick Cook’s PHASIC document.

‘testp’ Command

The ‘testp’ command is used to run the on-board test pulser, and its format is as follows:

testp  x  y  z

x sets the test pulser frequency:  freq = 1 / ( x/12500 + 1e-5 )  pulses per second

(the default at boot-up is currently 4e2 = 10 pulses per second)

y sets the DAC setting for PHA #0 (common test input to H1i and H1o)

z sets the DAC setting for PHA #1 (common test intput to H2, H3, H4, H5, H6)

(the defaults at boot-up for y and z are 0)

The DAC settings (y and z) can be as follows:

00 to ff  (DAC voltages = 0V to .25V)

100 to 1ff  (DAC voltages = 0V to 5.00V)

If the test input capacitor and feedback capacitor are set to the same hex setting (as described above in the ‘tpfbsel’ command section), the low range of DAC voltages will stimulate the entire HG channel, and the high range of DAC voltages will stimulate the entire LG channel.

The test pulser can be run in automatic mode, using this command:  testp auto

This will step through each of the DAC settings (one step per minute) at the last selected pulser frequency.