STEREO/SIT

Flight Software Requirements Traceability Matrix

Last Modified July 12, 2005

| Req. Sec. #(s) | Req. # | Requirement Description | Software Routine(s) | Test Case | Comments | Comp. Date |
| --- | --- | --- | --- | --- | --- | --- |
| 3.2 3.4 |  | Interrupt Processing 1-minute Timer interrupt | - | - |  |  |
|  | 3.4.1.1 | 1-minute timer interrupt responds by setting end-of-frame flag. | Int5sr HandleMajor | SEP boot CPT |  |  |
| 3.5 |  | SIT CPU24 Soft Reset | - | - |  |  |
|  | 3.5.1.1 | Initialize all the UART’s. | Start initvars | CPT |  |  |
|  | 3.5.1.2 | Initialize and clock out all the hardware setup serial strings. | Start | CPT |  |  |
|  | 3.5.1.3 | Clear all software & hardware counters, queues and output packet buffers. | Init_All | CPT |  |  |
|  | 3.5.1.4 | Wait for end-of-frame flag, clear it and start the main processing loop. | Int5sr HandleMajor | CPT |  |  |
| 3.2 3.6 |  | Interrupt Processing Science Data Acquisition | - | - |  |  |
|  | 3.6.1.1 | Respond to the PHA event interrupt by reading a PHA event from the front end logic. | Int3sr | CPT Alpha |  |  |
|  | 3.6.1.2 | Store each PH event in a queue using first-in-first-out ordering. | Enqueue | CPT Alpha |  |  |
|  | 3.6.1.3 | Count all PH events read from the front end logic. | Proc_SIT_Evnts | CPT Alpha |  |  |
| 3.7 |  | Science Data Processing | - | - |  |  |
|  | 3.7.1.1 | Select the PH events from each priority class and store them in a sample buffer. | Proc_SIT_Evnts | CPT Alpha |  |  |
|  | 3.7.1.2 | Determine the species, energy and priority level by using a 2 dimensional detector response matrix and priority table. | Proc_SIT_Evnts | CPT Alpha |  |  |
|  | 3.7.1.3 | Respond to the EOF reset by resetting the software counters | PostFormat | CPT Alpha |  |  |
|  | 3.7.1.4 | Respond to the EOF reset by resetting the hardware counters | PostFormat | CPT Alpha |  |  |
|  | 3.7.1.5 | Respond to the EOF reset clearing all the event queues. | Init_All | CPT Alpha |  |  |
| 3.8 |  | Beacon Data Processing | - | - |  |  |
|  | 3.8.1.1 | Calculate beacon data every 60 seconds. | Proc_SIT_Evnts | CPT Alpha |  |  |
|  | 3.8.1.2 | Calculate beacon data for specific species and energy ranges. | Proc_SIT_Evnts | CPT Alpha |  |  |
| 3.9 |  | Housekeeping and Status Data Acquisition | - | - |  |  |
|  | 3.9.1.1 | Read the SIT specific software status information from SEP Central. |  | CPT Alpha | N/A |  |
|  | 3.9.1.2 | Read SIT command table information from SEP Central. |  | CPT Alpha | N/A |  |
|  | 3.9.1.3 | Read SIT software housekeeping information from SEP Central. |  | CPT Alpha | N/A |  |
|  | 3.9.1.4 | Format SIT status information for the science data packet. | FormatTM | CPT Alpha |  |  |
|  | 3.9.1.5 | Format SIT software command table information for the science data packet. | FormatTM | CPT Alpha Scripts |  |  |
|  | 3.9.1.6 | Format SIT software housekeeping information for the science packet. | FormatTM | CPT Alpha |  |  |
|  | 3.9.1.7 | Format the housekeeping and status data into a packet of 272 bytes. | FormatTM | CPT Alpha |  |  |
| 3.2 3.10 |  | Interrupt Processing Science Data Formatting | - | - |  |  |
|  | 3.10.1.1 | Execute in response to the EOF flag being set. | Int5sr HandleMajor PreFormat | CPT Alpha |  |  |
|  | 3.10.1.2 | Retrieve the rate counters and the live time from memory. | check_ratemode | CPT Alpha |  |  |
|  | 3.10.1.3 | Retrieve the sample PH event data from a buffer. | Dequeue | CPT Alpha |  |  |
|  | 3.10.1.4 | Format the SIT science data (rates and PH events) into science data packets. | FormatTM | CPT Alpha |  |  |
|  | 3.10.1.5 | Format 12 science packets accumulated over 1 minute. | FormatTM | CPT Alpha |  |  |
|  | 3.10.1.6 | Format each science packet to be 272 bytes in length, which include the CCSDS header. | FormatTM | CPT Alpha |  |  |
|  | 3.10.1.7 | Transmit the science data packets to the SEP Central via the data-out UART at the rate of 12 packets per minute. | Int4sr StartTMxmit HandleTMbyte | CPT Alpha |  |  |
|  | 3.10.1.8 | Reset the end-of-frame flag. | Int5sr HandleMajor PostFormat | CPT Alpha |  |  |
| 3.2 3.11 |  | Interrupt Processing Command Processing | - | - |  |  |
|  | 3.11.1.1 | Respond to the serial command interrupt by reading the command bytes from the UART connection to the SEP Central and storing it in a buffer. | Int0sr Enqueue | CPT Alpha Scripts |  |  |
|  | 3.11.1.2 | Use the command buffer and lookup and retrieve the associated commands in a table or decode the command directly. | Dequeue iskeywd isCommand | CPT Alpha Scripts |  |  |
|  | 3.11.1.3 | Respond to commands by setting data table values. | InstrumentCommand HandleCommand | CPT Alpha Scripts |  |  |
|  | 3.11.1.4 | Execute the commands producing a status flag to indicate error conditions. | InstrumentCommand HandleCommand | CPT Alpha Scripts |  |  |
|  | 3.11.1.5 | Write the command status flag to the science data packet. | FormatTM | CPT Alpha Scripts | N/A |  |
|  | 3.11.1.6 | Respond to the serial command out interrupt by transmitting the command byte to the UART connection to SEP Central. | Int1sr Dequeue | CPT Alpha Scripts |  |  |
| 3.12 |  | Reliability | - | - |  |  |
|  | 3.12.1.1 | Able to detect error conditions. | (various) | CPT Alpha |  |  |
|  | 3.12.1.2 | Set flags to indicate error conditions. | (various) | CPT Alpha |  |  |
|  | 3.12.1.3 | Write the error flag to the science data packet. | FormatTM | CPT Alpha |  |  |
|  | 3.12.1.4 | Remain in operational state following an error condition. | (various) | CPT Alpha |  |  |
|  | 3.12.1.6.1 | Maintain a command table containing all variable settings (thresholds, gains, modes, etc.) | command handleCommand | CPT Alpha |  |  |
|  | 3.12.1.6.2 | Calculate a checksum on the variable setting command table. | command handleCommand | CPT Alpha | SEP Central handles verifying checksums on commands sent |  |
|  | 3.12.1.6.3 | Write the command table checksum to the science packet. | FormatTM | CPT Alpha | SEP Central handles verifying checksums on commands sent |  |
|  | 3.12.1.6.4 | Monitor the command table for changes in status, if a change occurs, set a flag. | command handleCommand | CPT Alpha Scripts |  |  |
|  | 3.12.16.5 | Write the command table status flag to the science data packet. | FormaTM | CPT Alpha Scripts |  |  |
| 4.1 |  | GSE – Boot Code loading | - | - |  |  |
|  | 4.1.1.1 | Ability to load boot-up code and tables. | Tbug, tmon | Display |  |  |
| 4.2 |  | Display SIT Data Bytes | - | - |  |  |
|  | 4.1.2.1 | Retrieve the data packets via the UART. | SPiT | Display |  |  |
|  | 4.1.2.2 | Retrieve data packets via the TCP/IP protocol and Windows sockets. | Communicator WinMac -MyWinsock class | Display |  |  |
|  | 4.1.2.3 | Format the data packets into the LECR format. | WinMac- MyWinsock class | Processing option |  |  |
|  | 4.1.2.4 | Display the contents of the data packets in a readable format. | Communicator WinMac - CWmacView class | Various packet displays |  |  |
|  | 4.1.2.5 | Selection of data packet quantities for display. | WinMac- CSitCommandingDlg class | Display mode options |  |  |
|  | 4.1.2.6 | Ability to create and write the LECR format to a data file. | WinMac- MyWinsock class | Conversion option |  |  |
|  | 4.1.2.7 | Allow command file setup and processing | Communicator WinMac- CSitCommandingDlg class | GSE and Commanding option |  |  |
| 4.1.3 |  | Plotting of SIT CPU24 Data Bytes | - | - |  |  |
|  | 4.1.3.1 | Ability to create 2 dimensional plots from the formatted SIT science data file. | WinMac- CWmacView class | Plotting option |  |  |
|  | 4.1.3.2 | Selection of science data quantities for producing plots. | WinMac – axseldlg class | Plotting options |  |  |
| 4.1.4 |  | GSE – Command Processing To and From the SIT CPU24 | - | - |  |  |
|  | 4.1.4.1 | Ability to retrieve command bytes from the SIT CPU24 UART. | SpiT | GSE and Commanding option |  |  |
|  | 4.1.4.2 | Ability to send command bytes to the SIT CPU24. | SpiT | GSE and Commanding option |  |  |