SITCPU G-Bus Read Map:

g@0  read Interrupt Control and Status

bit 23	logical OR of enabled interrupt lines

bit 22-12	status of interrupt lines 10-0

bit 11-1	enables for interrupts 10-0 (#0 is highest priority)

bit 0		global interrupt enable (1=enabled)

g@1  read Command UART Receiver Data (sit_cmd_in; clears interrupt 0)

bit 23-8	unused

bit 7-0	Tx Data

g@2  read Zero constant

g@3  read One constant

g@4  read Event Data

bit 23	Eonly option

bit 22	Gain/Ramp; 1=High gain, 0=Low

bit 21-20	TOF Flag bits, ie TOF Data [10:9]

bit 19-9	Energy Data (High/Low gain according to bit22)

bit 8-0	TOF Data[8:0]

g@5  read TOF return data

bit 23-17	unused

bit 16	TOF return data done

bit 15-0	returned data from TOF

g@6  read SIT Control

bit 23-10	unused spares

bit 9		Eonly option

bit 8		HVPS Enable

bit 7-0	HVPS DAC Level

g@7  read Housekeeping Control & Data

bit 23-12	unused

bit 11	HK comparator data

bit 10-8	HK MUX address

bit 7-0	HK DAC level

g@8  read Stack Status

bit 3		Data stack overflow condition

bit 2		Data stack underflow condition

bit 1		Return stack overflow condition

bit 0		Return stack underflow condition

g@9 to g@15 are unused

SITCPU G-Bus Write Map:

g!0  write Interrupt & Clock Control

bit 23	stop pclk

bit 22-11	unused

bit 10-1	enables for interrupts 10-0 (#0 is highest priority)

bit 0		global interrupt enable (1=enabled)

g!1  write Command UART transmit data (sit_cmd_out; clears interrupt 1)

bit 23-8	unused

bit 7-0	Tx Data

g!2  write Science Data UART transmit data (sit_data_out; clears interrupt 2)

bit 23-8	unused

bit 7-0	Tx Data

g!3  unused

g!4  write Interrupt Reset – set bit, poll for condition gone, then clr bit

bit 4		timer

bit 3		stack problem

bit 2		minute sync

bit 1		second sync

bit 0		event

g!5  write TOF Control

bit 23-22	unused

bit 21-17	TOF address

bit 16	r/w (1=read)

bit 15-0	Control Data to TOF

g!6  write SIT Control

bit 23-11	unused

bit 10	Eonly option

bit 9		HVPS Load

bit 8		HVPS Enable

bit 7-0	HVPS DAC Level

g!7  write Housekeeping Control

bit 23-11	unused

bit 10-8	HK MUX Address

bit 7-0	HK DAC Level

g!8  Timer load cnt

bit 23-8	unused

bit 7-0	Timer count (1-255), lsb = 1.024ms

g!9 to g!15 are unused

SITCPU Interrupt assignments (0=highest priority):

int 0		SIT Command UART receiver data ready

int 1		SIT Command UART transmitter buffer empty

int 2		SIT Science Data UART transmitter buffer empty

int 3       event

int 4		second sync

int 5		minute sync

int 6		stack problem

int 7		timer