STEREO/IMPACT/SIT

SIT Acoustic Door Opening Procedure

Ver. 2.0  02/22/05

Unit:			  Test:					  Date:

1.  PURPOSE

This procedure opens the SIT acoustic cover.

The procedure takes about 15 minutes to set up and 1 minute to perform and can be interleaved with other procedures from other sensors.

2.  REQUIREMENTS

2.1  The procedure requires the following equipment:

1) Lab power supply capable of 28v, 1.5A

2) Digital scope

3) IMPACT TiNi Actuator GSE

4) BNC cable, banana leads (2), 9-pin cable to SIT actuator harness

5) DVM

3. PROCEDURE

3.1	Setup LVPS

Adjust LVPS for 28.0 v (+/- 0.5v) and 1.5A current limit (+.3/-0)

3.2	Setup Scope

Setup for single trigger, 5v/cm, 10ms/cm, set 0v on lower part of screen so 30v is on screen.  Adjust trigger for negative slope, dc trig at 27v or so.

3.3	Setup Actuator GSE

Set selector switch to position 9.

3.4	Connect System

Connect cables per attached figure.  Make sure polarity of power leads is correct.  Connect 9=pin harness to SIT connector on back of GSE.

3.5	Actuate

Turn on LVPS

Verify visible on scope by forcing trigger

Make sure SIT ready for door opening

Press button on front of TiNi GSE.

3.6	Verify

On scope face, verify trace goes down about 5 v for about 20 ms and then drops to zero:

Voltage drop:______________________

Duration:__________________________

Verify door opens completely

OK______________________________

Log opening in lab notebook/traveler for affected unit.

End of Procedure

Performed By