CPU24 Microprocessor User's Manual

Version 5 Actel for Stereo HET

8/2001  Text Modified for GAFC CPU24 RGB

Changed slot numbering

9/2001  Added second UART (transmit only)

Baud rates fixed at 57600

Added boot ROM, boot via uart, see boot.c for protocol

Added wait state for memory writes to increase address and data hold time

g!3 writes to test board LED’s

Both stacks are 17 deep

10/2001 Carry bit documentation corrected

Return stack now 33 deep

Parameter stack wraps around, like MISC6

6/2002  Second UART, TX only

PHA ASIC Interface

Sync signal interface

Livetime Counter

4/2003  Update for Actel Version 3, EM Board

5/2003  Add Stop Processor Clock control bit to g!0

Expand to 11 interrupts

Add timer

6/2003  Correct typo, correct timer period

8/2003  Update for Actel version 4

Update clock frequency and timer and test pulser periods

Add no_data_flag, bit 8 to g@9

Remove coincidence mode bits from g!4

Remove iclk, idata from g!4

Add g!9, coincidence and trigger mode bits, add rej_all

Add g!10, et and hazard timer bits

Add general purpose registers, x and y, at g addresses 14 and 15

10/2003 Update for Version 5 Actel

Test pulser period units, correct live time units

Chapter 1.	INTRODUCTION

1.1	General Information

CPU24 is a “Minimal Instruction Set Computer” design patterned after Mr. Chuck Moore's MuP21.  CPU24 has a 24-bit CPU core with dual stack architecture intended to efficiently execute Forth-like instructions.  The processor design is simple to allow implementation within field programmable gate arrays.

CPU24 employs a RISC-like instruction set with four 6-bit instructions packed into 24 bit words.  The most significant bit of each instruction designates an I/O Bus operation when set.  For I/O Bus instructions (the I/O bus will be referred to as the G bus) the second most significant bit specifies a write when set, read when cleared, while the remaining four bits specify the G bus address.  For non-G bus instructions the most significant bit is cleared and the remaining 5 bits specify 32 possible instructions.

Following is a list of CPU24 features:

*	24-bit address and data buses

*	6-bit RISC-like CPU instructions

*	4-deep instruction cache

*	17-deep data stack

*	33-deep return stack

*	Version 5 uses 71% of 54SX72A C-cells and 90% of the R-cells

*	Instruction rate is 6.4 million instructions per second

1.2 Architecture of CPU24 CPU

CPU24 has the following registers:

A	Address Register, supplying address for memory read and write

I	Instruction Register, holding instructions to be executed

P	Program Counter, pointing to the next program word in memory

R	Top of Return Stack

S	Top of Data stack

T	Accumulator for ALU

All registers are 24 bit wide.

The ACTEL implementation provides for a dedicated carry flip-flop that is modified by the add and shl instructions only.

CPU24 has two stacks:

S_stack	Data stack, 17 levels deep (including T)

R_stack	Return stack, 33 levels deep (including R)

The return stack is used to preserve return addresses on subroutine calls.  The data stack is used to pass parameters among the nested subroutine calls.

The following diagram shows the architecture of the CPU24 processor.  It shows the registers, the stacks, and the data paths among them.

Not shown in the diagram is the connection between T register and the external data bus.  When reading data from memory, the A register supplies the memory address to the address bus, and data is latch from the data bus into the T register.  When writing data into memory, the address is supplied by A register, and data is written to the data bus from the T register.

Figure 1.	The architecture of CPU24

Data Bus	    Address Bus

|		   ^		   ^

|		   |		   |

v		   |		   |

|-----|	|-----|	|-----|

|  I  |	|  P  |	|  A  |

|-----|	|-----|	|-----|

^		   ^

|		   |

v		   v

|-----------------------|-----|	|-----|	|-----|-----------------|

| Return Stack		|  R  |<--->|  T  |<--->|  S	| Data Stack 	|

|-----------------------|-----|	|-----|	|-----|-----------------|

^   |	 |

|   v	 v

|  |---------|

|  |   ALU   |

|  |---------|

|<------|

Chapter 2.	Device Characteristics

2.1	Version 5 Input and Output Signals

Input Signals:

tclk_in           32  MHz master clock

pclk_in           6.4 MHz instruction clock

eclk_in           6.4 MHz clock for event controller

het_reset_n       active low reset command

pwrup_reset       power up reset

het_cmd_in        Command UART input

het_frame_sync_n  The one second/minute sync signal

serboot           Mode input, high for serial boot, low for EEPROM boot

compout           ADC Comparator

spare_in          Spare inputs (3)

lop_or_a,     lop_or_b   Signals from PHA ASIC

rndn_or_a,    rndn_gor_0_a,

rndn_gor_1_a, rndn_gor_2_a

rndn_or_b,    rndn_gor_0_b,

rndn_gor_1_b, rndn_gor_2_b

pha_data          24-bit data bus from PHA ASIC

Output Signals:

pclk_out      wire to pclk_in

eclk_out      wire to eclk_in

reset_out

het_cmd_out   Status UART output

het_data_out  Data UART output

ram_en_n

mem_r_w_n

ram_addr      17-bit memory address

test_out      8-bit test port

high_rate     Test Output

debug_out     Test Output, event state machine or stack over/underflow

g5_out_14     Spare Output

g5_out_15     “

g5_out_16     “

sdata_n, sclk_n, sload_n, hk_dac[7:0]     DAC control signals

token_in      PHA ASIC Control Signals

read_reset, adc_read_sel, cmd_data_in, cmd_clk_in, cmd_reset_n

ctr_reset, pha_reset, clg, test_pulse, cmd_strobe, read_clk_in, pha_clk

Tri State Input/Output:

ram_data      24-bit memory data bus

2.2	Timing

All time periods noted in the following timing diagrams are in periods of the master clock.

Figure 3.	Timing of CPU24 instruction executions

Master Clock

|---	|	|----	|	|----	|	|----	|	|----	|	|----	|	|----

|	|	|	|	|	|	|	|	|	|	|	|	|

|	|----	|	|----	|	|----	|	|----	|	|----	|	|---- |

Slot0 Signal

|-----------|								|-----------|

| slot0	|  slot1	|  slot2	|  slot3	|  slot4	|  slot0	|

|		|-----------------------------------------------|		|----

fetch Instr   execute	   execute	   execute	   execute	 fetch instr

call, jump, jz, jnc

|-----------|		|-----------|

| slot0	|  slot1	|  slot0	|

|		|-----------|           |----------------------------------------

fetch Instr   execute	   execute	   execute	   execute	   execute ...

NOP and RET instructions can be in any of the four slots.  When these two instructions are executed, slot0 will be forced into the next slot, and the next instruction words will be fetched and then executed.

The CPU24 implementation contains a prioritized interrupt controller.  If an interrupt is pending an extra slot, slot5, is added to the sequence following slot4.  During slot5 the program counter is pushed to return stack and the interrupt vector is placed in the program counter.  Currently 11 interrupt lines, labeled int0 – int10 are implemented.  Int0 vectors to address 1, int1 to address 2, etc.  The highest priority int0 is currently assigned to the UART receive function, while the next highest priority int1, int2 are assigned to the UART transmit functions.  Once an interrupt is serviced via execution of slot5, servicing of interrupts is automatically disabled until the execution of an RTI instruction.  Immediately after the RTI execution, the highest priority pending interrupt (if any) will be serviced.

Chapter 3.	CPU24 Instruction Set

The CPU24 instruction set can be best explained using the register and data flow diagram as shown in Figures 1 and 2.  The T register is the center of the ALU, which takes data from the T and S registers and routes the results back to the T register.   The contents of T can be moved to the A register, pushed on the data stack S, and pushed on the return stack S.

The T register connects the data stack and the return stack as a large shift register.  Data can be shifted towards the return stack by the PUSH instruction, and shifted towards the data stack by the POP instruction.

The top of the data stack wraps around to the bottom of the data stack for all data stack pop operations.

Register A holds a memory address, which is used to read data from memory into the T register, or write the data in T register to external memory.  The address in A can be auto incremented, so that CPU24 can conveniently access data arrays in memory.

P is the program counter and it holds the address of the next instruction to be fetched from the memory.  After an instruction is fetched, P is auto incremented and ready to read the next instruction.  When a CALL instruction is executed, the address in P is pushed on the return stack.  When a return (RET) instructions is executed, the previously saved address in R is popped back into P.  The execution sequence interrupted by CALL can now be resumed.

CPU24 is a microprocessor with 24-bit instructions.  Each instruction contains up to 4 6-bit machine codes.  The instruction fields in a program word can be shown as follows:

Bits:	23 22 21 20 19 18 17 16 15 14 13 12 11 10 09 08 07 06 05 04 03 02 01 00

| Instruction 1   | Instruction 2   | Instruction 3   | Instruction 4   |

There are 64 possible instructions in a 6-bit field.  Half of these are used for G-Bus access, and are specified by a one in the most significant bit of the six-bit field.  For G-Bus access instructions the next most significant bit specifies write if set, read if cleared, while the remaining 4 bits are the G-Bus address.  The G-Bus is intended to provide fast access to on-chip application specific functions such a timers, i/o registers, UART, general purpose registers, etc.  The non-G-Bus instructions are of four classes:

0	Transfer Instructions

1	Memory Access Instructions

2	ALU Instructions

3	Register Instructions

JUMP, CALL, JZ and JNC instructions must appear in Slot1 of a program word, ie. bits 23-18.  The last 18 bits 17-0 contain the address inside the current 256K word page.   They can access code within the current page.  To reach other pages of memory, you will have to push a 24-bit address on the return stack and execute the RET instruction.

The transfer instructions thus has the following forms:

JUMP	aaaaaa aaaaaa aaaaaa        CALL	aaaaaa aaaaaa aaaaaa

JZ	aaaaaa aaaaaa aaaaaa        JNC	aaaaaa aaaaaa aaaaaa

The conditional jump instruction JZ pops the number being tested in T.  The conditional jump instruction JNC causes a jump if the carry flip flop is cleared.  It is useful in multiple precision math operations.  JNC does not pop the T register, so its contents can be tested again.

Table 1.  CPU24 Machine Code

Code	Name		Function

Transfer Instructions

00	JUMP		Jump to 18 bit address.  Must in Slot1.

01	RET		Subroutine return.

02	JZ		Jump if T is 0.  Must in Slot1.

03	JNC		Jump if carry is reset.  Must in Slot1.

04	CALL		Call subroutine.  Must in Slot1.

05	NEXT		Jump if R is not 0.  Post-decrement R.

Pops R if R is 0.  Must be in Slot1.

06	TIMES		Repeat instruction word if R is not 0.  Post-decrement R.

Pops R if R is 0.

07	RTI		Return from interrupt

Memory Access Instructions

09	LDP		Push memory at A to T.  Increment A.

0A	LDI		Push in-line literal to T.

0B	LD		Push memory at A to T.

0D	STP		Pop T to memory at A.  Increment A.

0F	ST		Pop T to memory at A.

ALU Instructions

08	RR8		Rotate right T by 8 bits.

0C	NIP		Pop S, (Equivalent to SWAP DROP)

0E	OR		Pop S and OR it to T.

10	COM		Complement all bits in T.

11	SHL		Shift T left 1 bit.

12	SHR		Shift T right 1 bit.

13	MUL		Multiplication step.

14	XOR		Pop S and Exclusive OR it to T.

15	AND		Pop S and AND it to T.

16	DIV		Division step.

17	ADD		Pop S and add it to T.

Register Instructions

18	POP		Pop R to push T.

19	LDA		Push A to T.

1A	DUP		Duplicate T.

1B	OVER		S to T, push original T.

1C	PUSH 		Pop T to push R.

1D	STA		Pop T to A.

1E	NOP		Do nothing.

1F	DROP 		Pop T.

I/O Instructions

2n	G@n		Input to push T

3n	G!n		Output to pop T

CPU24 Instructions

JUMP

Code:				00

Usage:			00000 aaaaaa aaaaaa aaaaaa

Stack Effects:		none

Carry:			no change

Function:

Jump to the 18 bit address in the bit field 17-0 in the current 256K word page of memory.  It must be in slot 1 of a word.

Restriction:

This instruction allows the program to be redirected to any location within an 256K word page of memory.  It does not cross page boundaries.  To jump to locations outside of a memory page, one has to push the target address on the return stack and execute the RET instruction to effect a long jump.  This restriction also applies to CALL, JZ and JNC.  See also RET.

JZ

Code:				02

Usage:			000010 aaaaaa aaaaaa aaaaaa

Stack Effects:		( n -- )

Carry:			no change

Function:

Conditionally jump to the 18 bit address in the bit field 17-0 in the current 256K word page of memory, if the T register contains a 0.  It must be in slot 1 of a word.

The T register is destroyed and the data stack is popped back to T.  This instruction is different from JNC, which does not pop the data stack and removes T.

JNC

Code:				03

Usage:			000011 aaaaaa aaaaaa aaaaaa

Stack Effects:		( n -- n )

Carry:			no change

Function:

Conditionally jump to the 18 bit address in the bit field 17-0 in the current 256K word page of memory, if the Carry Flip Flop is reset.  It must be in slot 1 of a word.

The T register and the data stack are preserved.  This instruction is different from the instructions JZ, which pop the data stack and removes T.

NEXT

Code:				05

Usage:			000101 aaaaaa aaaaaa aaaaaa

Stack Effects:		( -- )

Carry:			no change

Function:

If R is non-zero jump to the 18 bit address in the bit field 17-0 in the current 256K word page of memory and post-decrement R.  If R is zero, pop R.  It must be in slot 1 of a word.

TIMES

Code:				06

Usage:                  any slot

Stack Effects:		( -- )

Carry:			no change

Function:

If R is non-zero jump back to the beginning of the current instruction word and post-decrement R.  If R is zero, pop R.

CALL

Code:				04

Usage:			000100 aaaaaa aaaaaa aaaaaa

Stack Effects:		( -- ; R: -- a )

Carry:			no change

Function:

Call a subroutine whose address is in the bit field 17-0 in the current 256K word page of memory.  It must be in slot 1 of a word

The address of the next word is pushed on the return stack.  When a return instruction in the subroutine is encountered, this address is popped off the return stack and the next word is executed to resume the interrupted execution sequence.

RET

Code:				01

Usage:			any slot

Stack Effects:		( -- ; R: a -- )

Carry:			no change

Function:

Pop the address of the top of the return stack into the program counter P, thus resume the execution sequence interrupted by the last CALL instruction.  Besides terminating a subroutine, this instruction may be used to effect a long jump to a location outside of the current memory page.

This instruction can be placed in any slot of a word.  The instructions before return are executed.  The instructions following return are ignored.

LDI

Code:				0A

Usage:			any slot

nnnnnn nnnnnn nnnnnn nnnnnn

Stack Effects:		( -- n )

Carry:			no change

Function:

Fetch the contents of the next word and push that number onto the data stack.  The program counter PC is incremented passing the next word.  This instruction allows a program to enter numbers onto the data stack for later use.

LD

Code:				0B

Usage:                  any slot

Stack Effects:		( -- n )

Carry:			no change

Function:

Fetch the contents of a memory location whose 24-bit address is in the A register and push that number onto the data stack.  The address in the A register is not modified.

LDP

Code:				09

Usage:                  any slot

Stack Effects:		( -- n )

Carry:			no change

Function:

Fetch the contents of a memory location whose 24-bit address is in the A register and push that number onto the data stack.  The address in the A register is then incremented to facilitate accessing the next memory.  It is most useful in reading values from a table in the memory.

LDA

Code:				19

Usage:                  any slot

Stack Effects:		( -- a )

Carry:			no change

Function:

Copy the contents in the A register to the T register.  The original content of the T register is pushed on the data stack.  With LDA and STA, the A register can serve as a scratch pad register to save and restore the contents of the T register.

ST

Code:				0F

Usage:                  any slot

Stack Effects:		( n -- )

Carry:			no change

Function:

Pop the number off the data stack and store it into the memory location whose 24-bit address is in Register A.  The address in the A register is not modified.

STP

Code:				0D

Usage:                  any slot

Stack Effects:		( n -- )

Carry:			no change

Function:

Pop the number off the data stack and store it into the memory location whose 24-bit address is in Register A.  The address in the A register is then incremented to facilitate the next memory access.  It is most useful in storing values to a table in the memory.

STA

Code:				1D

Usage:                  any slot

Stack Effects:		( a -- )

Carry:			no change

Function:

Pop S on the data stack and store it to the T register.  The original contents in the T register is copied into the A register.  This instruction initializes the A register so that it can be used to fetch data from memory or store data into memory.

NOP

Code:				1E

Usage:                  any slot

Stack Effects:		(  -- )

Carry:			no change

Function:

No operation.  This instruction will force the execute state to slot 0, to get the next word to be fetched and executed.

PUSH

Code:				1C

Usage:                  any slot

Stack Effects:		( n -- ; R: -- n )

Carry:			no change

Function:

Pop S on the data stack and store it to the T register.  The original contents in the T register is pushed onto the return stack.

POP

Code:				18

Usage:                  any slot

Stack Effects:		( -- n ; R: n -- )

Carry:			no change

Function:

Pop the R register on the return stack to the T register.  Original contents in T are pushed on the data stack.

Coding Example:

Exchanging A and T	lda push sta pop

Exchanging A and R	lda pop sta push

DUP

Code:				1A

Usage:                  any slot

Stack Effects:		( n -- n n )

Carry:			no change

Function:

Duplicate T register and push it on the data stack.

OVER

Code:				1B

Usage:                  any slot

Stack Effects:		( n1 n2 –- n1 n2 n1 )

Carry:			no change

Function:

S is transferred into T register.  The original contents in the T register is pushed onto the data stack.

DROP

Code:				1F

Usage:                  any slot

Stack Effects:		( n -- )

Carry:			 no change

Function:

Pop S on the data stack and store it to the T register.  The original contents in the T register are lost.

NIP

Code:				0C

Usage:                  any slot

Stack Effects:		( n1 n2 -- n2 )

Carry:			no change

Function:

Pop S, leaving T unchanged.

RR8

Code:				08

Usage:                  any slot

Stack Effects:		( n1 -- n2 )

Carry:			no change

Function:

All 24 bits in the T register are rotated right by 8 bits.  The least significant byte of T moves to the position of the most significant byte.

Useful for fast accessing of byte data and data formatting/packing.

COM

Code:				10

Usage:                  any slot

Stack Effects:		( n1 – n1* )

Carry:			no change

Function:

Complement all 24 bits in the T register.  This is a one's complement operation.

SHL

Code:				11

Usage:                  any slot

Stack Effects:		( n -- 2n )

Carry:			Bit 23 of T is shifted into carry

Function:

Shift all lower 24 bits in the T register to the left by 1 bit.  The bit 0 (least significant) is cleared.  Carry gets bit 23.

SHR

Code:				12

Usage:                  any slot

Stack Effects:		( n -- n/2 )

Carry:			no change

Function:

Shift the contents of the T register right by one bit.  The sign (bit 23) is preserved.

OR

Code:				0E

Usage:                  any slot

Stack Effects:		( n1 n2 -- n3 )

Carry:			no change

Function:

Pop S on the data stack and OR it with the T register.  All 24 bits in T are affected.

AND

Code:				15

Usage:                  any slot

Stack Effects:		( n1 n2 -- n3 )

Carry:			no change

Function:

Pop S on the data stack and AND it to the T register.  All 24 bits in T are affected.

ADD

Code:				17

Usage:                  any slot

Stack Effects:		( n1 n2 -- n1+n2 )

Carry:			change according to n1 plus n2

Function:

Pop S on the data stack and add it to the T register.  Add is unsigned.

MUL

Code:				13

Usage:                  any slot

Stack Effects:		( n1 n2 -- n1 n3 )

Carry:			no change

Function:

Conditionally add the S register on the data stack to the T register if bit 0 in A is set.  If bit 0 in A is reset, T register is not modified.  The T-A register pair is now shifted to the right by one bit.

This MUL instruction is useful as a multiplication step in implementing a fast software multiplication routine.  Repeating this instruction 24 times will multiply A and S and produce a 48-bit product in the T-A pair.  (T is normally initialized to zero prior to the multiply sequence.  However any non-zero initial value in T adds to the final result in the T-A pair.)

Coding Example:

Multiply two 24-bit unsigned integers.  Multiplicand is in S.  Multiplier is in A.

mul mul mul mul

mul mul mul mul

mul mul mul mul

mul mul mul mul

mul mul mul mul

mul mul mul mul

The 48-bit product is in T-A register pair and the multiplicand in S is preserved.

DIV

Code:				16

Usage:                  any slot

Stack Effects:		( n1 n2 -- n1 n3 )

Carry:			no change

Function:

Add the S register on the data stack to the T register.  If the addition produces a carry place the sum in T, otherwise leave T unchanged.  The T-A register pair is now shifted to the left by one bit.  Carry is shifted into A(0).

This DIV instruction is useful as a division step in implementing a fast software division routine.  Repeating this instruction 25 times (and then performing a shr) will divide a 48 bit number (positive, msb must be zero) originally in the T-A register pair by the negative of the number in S, leaving the result in A and remainder in T.

Coding Example:

Divide a 48-bit positive integer by a positive divisor.  The negated divisor is in S.

div div div div

div div div div

div div div div

div div div div

div div div div

div div div div

div shr

XOR

Code:				14

Usage:                  any slot

Stack Effects:		( n1 n2 -- n3 )

Carry:			no change

Function:

Pop S on the data stack and exclusive-OR it to the T register.  All 24 bits in T are affected.

RTI

Code:				07

Usage:                  any slot

Stack Effects:		( -- ; R: a -- )

Carry:			no change

Function:

Pop the address of the top of the return stack into the program counter P, to resume execution at completion of an interrupt service routine.  Re-enables slot5 interrupt servicing.

This instruction can be placed in any slot of a word.  The instructions before RTI are executed.  The instructions following return are ignored.

G@n

Code:				2n, where n is 4bit G-Bus address

Usage:                  any slot

Stack Effects:		( -- n1 )

Carry:			no change

Function:

Read G-bus address n and store in T, push original contents of T to data stack.

G!n

Code:				3n, where n is 4bit G-Bus address

Usage:                  any slot

Stack Effects:		( n1 -- )

Carry:			no change

Function:

Pop S from data stack into T.  Original contents of T are written to G-bus address n.

G-Bus Assignments:

g@0  read Interrupt Control and Status Register

g@1  read UART Receiver Data

g@2  read zero

g@3  read one

g@4  read PHA ASIC Data

g@5  read Live Time Counter

g@8  read Coincidence Signals

g@9  read stack over/underflow, Spare, and Compout bits

g@10 read Trigger Counter

g@14 read general register x

g@15 read general register y

g!0  write Interrupt Control and Status Register

g!1  write UART Transmit Data

g!2  write second UART Transmit Data

g!3  write to Test Port (lower 8 bits)

g!4  write to PHA ASIC Control Signals

g!5  write 3 Spare Output bits, 14-bit Test Pulser Period, units of 80 usec

g!6  write Interrupt Reset and Control bits

g!7  write DAC control signals

g!8  write timer period - 1, units of 0.64 msec, 8 bits,

g!9  write trigger, coincidence mode bits

g!10 write et and hazard timer bits

g!14 write general register x

g!15 write general register y

Interrupt Control and Status Register bits (g@0, g!0):

Bit0(lsb)	r/w	global interrupt enable (1 to enable)

Bit1		r/w	enable for interrupt 0 (highest priority)

Bit2		r/w	enable for interrupt 1

Bit3		r/w	enable for interrupt 2

Bit4		r/w	enable for interrupt 3

Bit5		r/w	enable for interrupt 4

Bit6		r/w	enable for interrupt 5

Bit7		r/w	enable for interrupt 6

Bit8		r/w	enable for interrupt 7

Bit9		r/w	enable for interrupt 8

Bit10		r/w	enable for interrupt 9

Bit11		r/w	enable for interrupt 10

Bit12		r	status of interrupt line 0

Bit13		r	status of interrupt line 1

Bit14		r	status of interrupt line 2

Bit15		r	status of interrupt line 3

Bit16		r	status of interrupt line 4

Bit17		r	status of interrupt line 5

Bit18		r	status of interrupt line 6

Bit19		r	status of interrupt line 7

Bit20		r	status of interrupt line 8

Bit21		r	status of interrupt line 9

Bit22		r	status of interrupt line 10

Bit23		r	logical OR of enabled interrupt lines

Bit23		w     stop processor clock

Interrupts are assigned:

int 0		UART receiver data ready

int 1		UART transmitter buffer empty

int 2		second UART transmitter buffer empty

int 3       event interrupt

int 4		second sync

int 5		minute sync

int 6		stack problem

int 7		timer

int 8-10	unused

The interrupt enable bits are all initialized to 0 by power-on reset.  Note that after performing an interrupt, the interrupt controller will (without clearing bit 0) disable further interrupt servicing until after the next RTI instruction is executed.  Interrupt lines 0, 1, and 2 are dedicated to the UART receive and transmit functions.  Interrupt line 0 is set after a character is received by the UART and is cleared by reading the data at Gbus address 1 (least significant 8 bits).  Interrupt lines 1(2) is set after the UART #1(2) transmitter buffer is empty is cleared by writing a character to Gbus address 1(2) (least significant byte).

Read of Gbus addresses 2 and 3 return 0 and 1 respectively.  (Special assembler words “zero” and “one” compile the instructions to read Gbus addresses 2 and 3.)

The Live Time Counter (g@5) is a 24-bit binary counter that counts 5 usec livetime ticks from the live time prescaler.  The counter is reset by the read instruction.  The prescaler counts at 6.4 MHz whenever the event readout state machine is waiting for a trigger.

The Coincidence signals (g@8) are latched at the end of the coincidence resolving time by the event state machine and are used to classify the event.  The signals are:

| bit | sig name | description |
| --- | --- | --- |
| 11 | hazard_ff | hazard if was a previous event within ____ usec |
| 10 | anti_stim_g8in_ff | event was generated by falling edge of test pulse |
| 9 | stim_g8in_ff | event was generated by rising edge of test pulse |
| 8 | rndn_gor_2_a_ff | not used in coincidence |
| 7 | rndn_gor_1_a_ff | PHASIC A gor used in high rate mode |
| 6 | rndn_gor_0_a_ff | PHASIC A gor used in normal rate mode |
| 5 | rndn_gor_2_b_ff | PHASIC B used in anticoincidence |
| 4 | rndn_gor_1_b_ff | PHASIC B gor used in high rate mode |
| 3 | rndn_gor_0_b_ff | PHASIC B gor used in normal rate mode |
| 2 | rndn_or_a | PHASIC A trigger signal |
| 1 | rndn_or_b | PHASIC B trigger signal |
| 0 | stop_req_event | event sm triggered by stop_req for commanding/rates |

The Coincidence Equations are:

mux_out_a = high_rate ? rndn_gor_1_a : rndn_gor_0_a;

mux_out_b = high_rate ? rndn_gor_1_b : rndn_gor_0_b;

logic_out = sel_or ? (mux_out_a | mux_out_b) : (mux_out_a & mux_out_b);

coin_valid = logic_out & (stim_g8in_ff | ~req_stim) &

~(rej_anti_stim & anti_stim_g8in_ff) &

~(rej_rndn_gor_2_b & rndn_gor_2_b_ff) &

~(rej_hazard & hazard_ff) & ~rej_all;

The Spare and Compout bits (g@9):

| bit | sig name | description |
| --- | --- | --- |
| 8 | no_data | No data for this event |
| 7:4 | stack_o/uflow | s_overflow, s_underflow, r_overflow, r_underflow |
| 3 | spare in 2 | Spare inputs |
| 2 | spare in 1 |  |
| 1 | spare in 0 |  |
| 0 | compout | ADC comparator output |

The Trigger Counter (g@10) is a 24-bit binary counter that counts triggers.  The counter is reset by the read instruction.  Triggers equation is:

(lop_or_a * ~dis_lop_or_a) | (rndn_or_a * ~dis_rndn_or_a) |

(lop_or_b * ~dis_lop_or_b) | (rndn_or_b * ~dis_rndn_or_b) | stop_req.

Note that stop requests are counted, can be subtracted out.

PHA ASIC Control bits (g!4):

| bit | signal | description |
| --- | --- | --- |
| 0 | stop_req | stop event sm for commanding/reading rates |
| 1:3 | unused |  |
| 4 | token_in | PHASIC readout and commanding control bits |
| 5 | read_reset |  |
| 6 | adc_read_sel |  |
| 7 | cmd_data_in |  |
| 8 | cmd_clk_in |  |
| 9 | cmd_reset_n |  |
| 10 | ctr_reset |  |
| 11 | pha_reset |  |
| 12 | clg |  |
| 13 | uptestpulse | program generated test pulse |
| 14 | cmd_strobe |  |
| 15 | read_clk_in |  |
| 16 | clkon | turn on PHASIC 32 MHz clock |
| 17 | uptpen | select microprocessor test pulse mode |
| 18 | upen | select microprocessor PHASIC readout mode |
| 19:23 | unused |  |

Test Pulse Period, Spare Output Bits, (g!5):

| bits | sig name | description |
| --- | --- | --- |
| 16 | spare_12 | Spare Output Bit |
| 15 | spare_11 | Spare Output Bit |
| 14 | spare_10 | Spare Output Bit, selects evproc_state (1) or {s_overflow, s_underflow, r_overflow, r_underflow} (0) as debug_out |
| 13:0 | tp_period | Test Pulser Period, units of 80 usec |

Interrupt Reset and Control bits, (g!6):

| bit | sig name | description |
| --- | --- | --- |
| 5 | reset_timer | Pulse to reset the timer interrupt |
| 4 | sp_reset | Pulse to reset the stack problem interrupt |
| 3 | min_reset | Pulse to reset the minute interrupt |
| 2 | sec_reset | Pulse to reset the second interrupt |
| 1 | einit | Pulse to reset the event controller |
| 0 | intack | Set high after event interrupt Set low after reading PHA data |

DAC control signals (g!7):

| bit | sig name | description |
| --- | --- | --- |
| 10 | sdata | serial data to 24-bit shift register |
| 9 | sclk | clock to shift register, data shifted on positive edge |
| 8 | sload | load data from shift register to output register |
| 7:0 | hk dac | housekeeping DAC data, the positive input to the ADC comparator |

The 24-bit shift register bits:  (msb first)

| bits | sig name | Description |
| --- | --- | --- |
| 23 | plsra_rng | PHASIC A test pulse level range control |
| 22 | plsrb_rng | PHASIC B test pulse level range control |
| 21 | hk_mux1 | select housekeeping ADC multiplexer output |
| 20 | hk_mux0 |  |
| 15:8 | plsrb_dac | PHASIC B test pulse level DAC |
| 7:0 | plsra_dac | PHASIC A test pulse level DAC |

The Housekeeping Multiplexer:

| hk_mux1 | hk_mux0 | Multiplexer Output |
| --- | --- | --- |
| 0 | 0 | preoutA |
| 0 | 1 | preoutB |
| 1 | 0 | temp1 |
| 1 | 1 | temp2 |

Trigger, coincidence mode bits (g!9):

| bit | sig name | description |
| --- | --- | --- |
| 0 | high_rate | set high rate coincidence mode |
| 1 | sel_or | select coincidence function: 1(or, 0(and |
| 2 | rej_rndn_gor_2 | select anticoincidence function |
| 3 | req_stim | require test pulse |
| 4 | rej_anti_stim | reject anti_stim pulse |
| 5 | rej_hazard | reject hazard events |
| 6 | dis_lop_or_a | disable lop_or_a from trigger equations |
| 7 | dis_lop_or_b | disable lop_or_b from trigger equations |
| 8 | dis_rndn_or_a | disable rndn_or_a from trigger equations |
| 9 | dis_rndn_or_b | disable rndn_or_b from trigger equations |
| 10 | reg_all | reject all events |

Timer control (g!10):

| bit | sig name | description |
| --- | --- | --- |
| 7:0 | et0 | Event timer 0, clg low to pharst low |
| 12:8 | et1 | Event timer 1, coincidence resolving time |
| 17:13 | et2 | Event timer 2, rndn-or low to clg low for rejected events |
| 22:18 | haz | Hazard timer |