STEREO

IMPACT

HET Limited Performance Test

Procedure

HET_LPT_C.DOC

Rev. C, 01/17/05

Larry Ryan

Tycho von Rosenvinge

Kristin Wortman

Date Run: ______________________________

Flight Model Location: ___________________

Flight Model Tested: _____________________

Flight Software Version:__________________

Data File Recorded:______________________

Performed By: __________________________

1. Test Description

This limited performance test procedure has been designed to run on either HET flight model (FM1 and FM2).  The WinMac-GSE software is required to send the appropriate commands for configuration and to view the HET packets to extract the relevant information for verification.

HET should be powered with the high voltage bias applied to the detectors, and the HET flight code should be booted with the HET tables successfully loaded.  The HET flight model should be in default boot configuration before running any test.  If previous tests were conducted, then HET should be rebooted before running any further tests.

The results of these tests will verify that the HET flight model is operational and the flight software is accepting and processing commands.

2.  Housekeeping Data

Record the housekeeping data for the seven HET detectors.  If HET has just been booted, it will take 5-7 minutes for all housekeeping data to come through.

Start Time: _____   HET Temperature #1 _____   HET Temperature #2 _____

Data from HK (dec) page:

|  | H1i | H1o | H2 | H3 | H4 | H5 | H6 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| PHASIC |  |  |  |  |  |  |  |
| Channel (FM1) |  |  |  |  |  |  |  |
| Preamp |  |  |  |  |  |  |  |
| HG Thresh (FM1) |  |  |  |  |  |  |  |
| LG Thresh (FM1) |  |  |  |  |  |  |  |
| Leakage |  |  |  |  |  |  |  |

The following are the expected values:

|  | H1i | H1o | H2 | H3 | H4 | H5 | H6 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| PHASIC | 0 | 0 | 1 | 1 | 1 | 1 | 1 |
| Channel (FM1) | 1 | 11 | 3 | 5 | 7 | 9 | 12 |
| Channel (FM2) | 1 | 10 | 2 | 5 | 7 | 10 | 13 |
| Preamp (volts) | ~4.40 | ~4.40 | ~4.40 | ~4.40 | ~4.40 | ~4.40 | ~4.40 |
| HG Thresh (FM1) | 284 | 220 | 36 | 188 | 140 | 180 | 100 |
| HG Thresh (FM2) | 192 | 244 | 124 | 120 | 68 | 68 | 30 |
| LG Thresh (FM1) | 176 | 192 | 112 | 8 | 96 | 112 | 248 |
| LG Thresh (FM2) | 192 | 192 | 44 | 56 | 64 | 52 | 52 |
| Leakage (uA) | <0.5 | <0.5 | <0.5 | <2.0 | <2.0 | <2.0 | <1.0 |

3.  Singles Rates / Spurious Events

Record the H1-H6 singles rates (low gain and high gain) for three consecutive major frames.  The high gain singles rates should be < 100/min., and the low gain singles rates should be < 5/min.

|  | High-Gain Singles Rates for 3 major frames | Low-Gain Singles Rates for 3 major frames |
| --- | --- | --- |
| Mjr Fr # |  |  |  |  |  |  |
| H1i |  |  |  |  |  |  |
| H1o |  |  |  |  |  |  |
| H2 |  |  |  |  |  |  |
| H3 |  |  |  |  |  |  |
| H4 |  |  |  |  |  |  |
| H5 |  |  |  |  |  |  |
| H6 |  |  |  |  |  |  |

Record the following rates for one major frame.   Major Frame #: ____________

| Rate Counter | Expected Counts | Actual Counts | Rate Counter | Expected Counts | Actual Counts |
| --- | --- | --- | --- | --- | --- |
| Livetime | ~12 x 106 |  | Stop heavies | 0 |  |
| Trigger | <300 |  | Pen H | 0 |  |
| Coincidence | 0 |  | Pen He | 0 |  |
| Events | 0 |  | Pen heavies | 0 |  |
| Singles que | 0 |  | Invalid | 0 |  |
| Stop que | 0 |  | H1 I and O | 0 |  |
| Pen que | 0 |  | Inconsist. | 0 |  |
| Stop H | 0 |  | H1 not first | 0 |  |
| Stop He | 0 |  | Stim evt cnt | 0 |  |

4.  Event Identification / Commanding

4.1.  Stopping H Events

Send the following HET commands:

FM1					FM2

tpfbsel 0 b 116			tpfbsel 0 a 116

tpfbsel 1 3 116			tpfbsel 1 2 116

testp 4e2 2d 1e			testp 4e2 2d 1e

Record the following rates counters.  All other rate counters should read 0.

Major Frame #  ___________________

| Rate Counter | Expected Counts | Actual Counts |
| --- | --- | --- |
| Coincidence | ~600 |  |
| Stop que | ~600 |  |
| Stop H | ~600 |  |
| Stim evt cnt | ~600 |  |

4.2.  Stopping He Events

Send the following HET commands:

FM1					FM2

tpfbsel 0 b 6				tpfbsel 0 a 6

tpfbsel 0 1 116			tpfbsel 0 1 116

tpfbsel 1 5 12c			tpfbsel 1 5 12c

testp 4e2 10f 1e			testp 4e2 10f 1e

Record the following rates counters.  All other rate counters should read 0.

Major Frame #  ___________________

| Rate Counter | Expected Counts | Actual Counts |
| --- | --- | --- |
| Coincidence | ~600 |  |
| Stop que | ~600 |  |
| Stop He | ~600 |  |
| Stim evt cnt | ~600 |  |

4.3.  Stopping Z>2 Events

Send the following HET commands:

FM1					FM2

tpfbsel 0 1 6				tpfbsel 0 1 6

tpfbsel 0 b 116			tpfbsel 0 a 116

tpfbsel 1 5 11c			tpfbsel 1 5 11c

testp 4e2 179 3d			testp 4e2 179 3d

Record the following rates counters.  All other rate counters should read 0.

Major Frame #  ___________________

| Rate Counter | Expected Counts | Actual Counts |
| --- | --- | --- |
| Coincidence | ~600 |  |
| Stop que | ~600 |  |
| Stop heavies | ~600 |  |
| Stim evt cnt | ~600 |  |

4.4.  Penetrating H Events

Send the following HET commands:

FM1					FM2

tpfbsel 1 3 126			tpfbsel 1 2 126

tpfbsel 1 7 11c			tpfbsel 1 7 11c

tpfbsel 1 9 11c			tpfbsel 1 a 11c

tpfbsel 1 c 116			tpfbsel 1 d 116

testp 4e2 17 b			testp 4e2 16 a

Record the following rates counters.  All other rate counters should read 0.

Major Frame #  ___________________

| Rate Counter | Expected Counts | Actual Counts |
| --- | --- | --- |
| Coincidence | ~600 |  |
| Pen que | ~600 |  |
| Pen H | ~600 |  |
| Stim evt cnt | ~600 |  |

Send the following HET commands:

FM1					FM2

tpfbsel 0 1 6				tpfbsel 0 1 6

tpfbsel 0 b 6				tpfbsel 0 a 6

tpfbsel 1 3 6				tpfbsel 1 2 6

tpfbsel 1 5 c				tpfbsel 1 5 c

tpfbsel 1 7 c				tpfbsel 1 7 c

tpfbsel 1 9 c				tpfbsel 1 a c

tpfbsel 1 c 6				tpfbsel 1 d 6

testp 4e2 0 0				testp 4e2 0 0